## Slide 1
INTRODUCTION
CCD vs CMOS
Compare CCD and CMOS image sensors with technical accuracy, defining engineering trade-offs, using visual comparison tools, and presenting findings in a structured and professional format.
CCD
CMOS
Every digital camera relies on an image sensor to convert light into an electrical signal
Choice of sensor directly affects image quality, speed, power consumption, and system cost
Technical Presentation

## Slide 2
AIM
Purpose of This Comparison
To study and compare the architecture, working principles, and performance characteristics of CCD and CMOS image sensors, in order to identify their key engineering trade-offs and determine their suitability for different imaging and computer vision applications.
CCD
CMOS
Understand how each sensor converts light into a digital signal
Compare power, speed, cost, noise, and dynamic range
Recommend the right sensor for a given application

## Slide 3
ARCHITECTURE
How Each Sensor Reads Out an Image
CCD
Charge-domain, serial readout
Pixel array → shift register → single output amplifier → ADC
Photodiode-only pixels; charge shifts row by row to one amplifier
One shared amplifier ⇒ uniform gain, low fixed-pattern noise
Native global shutter — all pixels expose simultaneously
CMOS
Active-pixel, parallel readout
Pixel array → in-pixel amps → column-parallel ADCs → digital bus
Each pixel has its own amplifier (3T/4T design)
Column-parallel ADCs digitize many pixels simultaneously
Standard CMOS fab integrates logic, timing, and ADC on-die

## Slide 4
OBJECTIVES
What This Comparison Sets Out to Establish
1
Explain the architecture
Describe how CCD and CMOS sensors convert light to a digital signal, and where their signal paths diverge
2
Identify engineering trade-offs
Quantify differences in power, speed, noise, dynamic range, and cost between the two technologies
3
Map technology to application
Determine which sensor architecture best fits a given use case, from scientific imaging to consumer devices
4
Support informed sensor selection
Provide a clear decision framework for engineers choosing between CCD and CMOS in system design

## Slide 5
RESULT
Comparative Findings
Relative performance across six design dimensions (1 = weakest, 10 = strongest)
Chart: 
| Dynamic Range | Power Efficiency | Readout Speed | Cost Efficiency | Low-Light Noise Perf. | On-Chip Integration
CCD | 8 | 3 | 4 | 3 | 8 | 3
CMOS | 7 | 9 | 9 | 9 | 7 | 9
CCD leads on
Dynamic range and low-noise uniformity — the single-amplifier path keeps output consistent pixel to pixel.
CMOS leads on
Speed, power, cost, and integration — parallel column ADCs and on-die logic suit high-volume systems.

## Slide 6
CONCLUSION
Summary & Recommendation
Choose CCD when …
Signal uniformity and dynamic range matter most
True global shutter is required
Power and cost are secondary concerns
Choose CMOS when …
Power, size, and cost are primary constraints
High frame rate or on-chip processing is needed
Production volume favors standard fabrication
Key takeaway
CCD and CMOS solve the same problem — converting light into a digital signal — through fundamentally different readout architectures. CCD's serial, single-amplifier design yields uniform, low-noise images but at higher power and cost. CMOS's parallel, in-pixel design trades a little uniformity for speed, efficiency, and integration. Backside-illuminated and stacked CMOS have closed most of the historical quality gap, making CMOS the default choice for nearly all modern systems, while CCD remains relevant for specialized scientific and precision-imaging applications.